## Slide 1
INTERIM PRESENTATION · REMOTE SENSING 2026 OCN 4704
Mars Global Mosaic
Mapping Lava Flows, Fluvial Channels, and Impact Craters in Visible and Infrared
Logan Edwards
Status as of 26 October 2026
Ius Chasma, 271–286°E: Viking MDIM 2.1 colour on this project's 100 m grid

## Slide 2
THE QUESTION
Project Goals
Assemble one co-registered visible and thermal-infrared mosaic of Mars in ArcGIS Pro, over the ±60° band the THEMIS night mosaic covers (86.6% of the surface), and use it to map lava flows, fluvial channels and impact craters.
1
Put Viking visible colour, THEMIS day and night infrared and HRSC/MOLA topography on one grid over ±60°.
2
Map the three landform families from that stack, first in a type area (Ius Chasma), then across ±60°.
3
Test whether thermal infrared separates surfaces that visible light cannot.
4
Score every product against something it never saw: held-out hand labels, the IAU crater gazetteer and the USGS geologic map.
Mars Global Mosaic · Interim presentation
2

## Slide 3
THE DATA
Relevant Spectral Bands
Band or product | Wavelength | Cell | What it contributes
Viking MDIM 2.1 R, G, B | visible, ~0.4–0.7 µm | 232 m | Albedo: bright dust, dark basalt; not stretched by region, so regional differences are real.
THEMIS Day IR (v12) | thermal IR, 6.8–14.9 µm | 100 m | Daytime temperature. Ground that is bright in visible stays cooler by day (r −0.49 at Ius).
THEMIS Night IR (v14, ±60°) | thermal IR, 6.8–14.9 µm | 100 m | Night temperature: rock holds heat. The band least like the others, ¦r¦ ≤ 0.12.
HRSC/MOLA blended DEM | altimetry + stereo | 200 m | Slope in degrees, local relief, hillshade, flow routing, closed-depression depth.
Diurnal contrast index | day − night, relative | 100 m | Separates materials inside one area; not thermal inertia, not comparable across the planet.
Mars Global Mosaic · Interim presentation
3

## Slide 4
THE DATA
Why Fuse Them: Three Independent Dimensions
Ius Chasma, r | Viking R | Viking G | Viking B | Day IR | Night IR
Viking R | 1 | +0.960 | +0.925 | −0.486 | −0.121
Viking G | +0.960 | 1 | +0.993 | −0.496 | −0.085
Viking B | +0.925 | +0.993 | 1 | −0.488 | −0.068
Day IR | −0.486 | −0.496 | −0.488 | 1 | +0.105
Night IR | −0.121 | −0.085 | −0.068 | +0.105 | 1
The three Viking bands behave as one (r 0.93–0.99); day IR adds a second dimension and night IR a third. That is the measured case for fusing them.
Each cell is shaded by the strength of the correlation: the brighter, the more the two bands repeat each other.
Mars Global Mosaic · Interim presentation
4

## Slide 5
WHERE IT STANDS
Project Tasks and Percent Complete
#
Task
Where it stands
13 Sep → now
Now
1
Scope, targets and type area
Two type areas, Ius Chasma and Athabasca Valles; the ±60° extent
100%
2
Raster acquisition
Three global mosaics plus the THEMIS night IR mosaic
100%
3
Statistics, stretches, pyramids
Done for every product; pyramids on the four source globals took 26 min
100%
4
Grouped mosaic viewer
Done
100%
5
DEM terrain derivatives
Slope rebuilt in degrees for the type area and ±60°
100%
6
Image-gradient products
Slope run on imagery, not the DEM; relabelled as gradient and not used
100%
7
Jezero context
Hosted services only; the dead HiRISE link removed
100%
8
Classification
±60° SVM on hand-drawn labels, 200 m: 73.8%, κ 0.58 held out; seven classes proposed
75%
9
CRS harmonisation
Done: one 100 m / 200 m grid over ±60°
100%
10
Visible + IR composite
Done: type area; 7-band ±60° stack
100%
11
Landform digitising
512 training polygons drawn; landform classes set up but empty; candidates ready to review
10%
12
Crater inventory
Robbins catalogue in the project (385,049); 465,354 closed depressions ≥ 1 km at ±60°
60%
13
Map layouts
17 map layouts with graticules (none in September)
85%
14
Report and presentations
Prospectus and Presentation 1 delivered; interim built to the 26 Oct cut; final paper and deck drafted
60%
Bar: percent complete toward the final. Light blue: done by 13 September; blue: added since; dark: still to do.
Mars Global Mosaic · Interim presentation
5

## Slide 6
WHERE IT STANDS
Processing Completed Since the Last Report
When | What | Outcome
18 Sep | Night IR acquired; type-area stack; slope on a metric grid | Four inputs on one 100 m grid, 100% co-valid; slope in degrees
19 Sep | ±60° grids and diurnal contrast index | 15.2 bn px in 36.3 min
19 Sep | Channel and crater candidates, Ius; basins at ±60° | 2,610 channels; 1,685 closed depressions; 5,144 basins ≥ 20 km
24–30 Sep | Global composites built in ArcGIS Pro | Two runs finished: 2 h 52 m and 3 h 10 m
29 Sep | Hand-drawn training polygons; SVMs | Four classes; two ±60° maps
2–3 Oct | First SVM maps checked; corrected stack scored held out | Tile artefact, mostly elevation; then 73.5%, κ 0.58
6–7 Oct | Backup to GitHub; class codes | Public repository; pixel = class code
8 Oct | Reference data, Athabasca, tests T1–T3 and T8 | Thermal adds +1.3 points; ten layouts
8–9 Oct | Digitising by review; tests T4–T7; validation sheet | No support for H1–H3 or a tributary count; 12 layouts
13–15 Oct | Pyramids; ±60° craters and channels ≥ 1 km; 180° DEM fix | 465,354 closed depressions, 969,822 channel segments
14–16 Oct | 200 m classification; T1 with Pro's SVM; the published map | 73.8%, κ 0.58; thermal adds +1.36 and +1.97 points
19–21 Oct | Deep learning: a box detector, then a U-Net over ±60° | U-Net 98.9%, κ 0.98 held out, as terrain provinces
22–23 Oct | The 512 labels audited; seven classes proposed | Five Crater labels are volcanoes; 1,086 proposals to review
Mars Global Mosaic · Interim presentation
6

## Slide 7
PRELIMINARY RESULTS
What the data show so far
Every map is a layout in the ArcGIS project, exported fresh for this deck.
86.6%
of the planet inside the ±60° analysis extent
73.8%
held-out accuracy of the published landform map, κ 0.58
+1.36
points of accuracy the thermal bands add, ArcGIS Pro's SVM at 200 m
465,354
closed depressions ≥ 1 km mapped across ±60°
Ius Chasma, 271–286°E: THEMIS night IR on this project's 100 m grid

## Slide 8
THE DATA
The analysis extent and the two type areas
The analysis covers ±60° latitude, 86.6% of the planet: the THEMIS night mosaic's coverage
Two type areas: Ius Chasma (canyon and tributaries) and Athabasca Valles (flood lava)
Orange: the USGS geologic map's volcanic units, used as the lava-flow reference
Mars Global Mosaic · Interim presentation
8

## Slide 9
THE DATA
The mosaic at ±60°
All four datasets on one 200 m grid
Composite Bands failed four times on the global rasters; projecting first and bounding the extent fixed it
Mars Global Mosaic · Interim presentation
9

## Slide 10
THE DATA
Ius Chasma type area: visible and night IR
Left, Viking visible colour; right, THEMIS night IR. 271–286°E, 6–13°S: canyon walls, plateau, Louros Valles
Same 100 m grid, every pixel valid in all five bands
Night IR barely correlates with any other band (|r| ≤ 0.12), so it adds information the others lack
Mars Global Mosaic · Interim presentation
10

## Slide 11
THERMAL SIGNAL
Can the thermal pair map material across ±60°?
Viking red separates the dusty provinces from the rocky ones by 47.67 DN
THEMIS day and night IR separate them by −0.19 and +0.02 DN; the index, over seven provinces, by −0.0009
Every province repeats the whole mosaic's mean and spread, because both THEMIS mosaics were stretched region by region
Across the planet, the material signal is in visible albedo
Mars Global Mosaic · Interim presentation
11

## Slide 12
THERMAL SIGNAL
Checked against calibrated thermal inertia (TES)
Viking albedo follows calibrated thermal inertia across the planet (r −0.36)
Night IR and the diurnal-contrast index follow it weakly, and only inside regions (|r| ≈ 0.1)
Day IR does not follow it, and across the planet neither THEMIS mosaic does
At TES's ~3 km cells the material signal is in visible albedo; thermal IR adds little
Mars Global Mosaic · Interim presentation
12

## Slide 13
CRATERS
Craters at ±60°: closed depressions ≥ 20 km
5,144 basins found by fill depth in 48 s
68% of 117 IAU craters ≥ 100 km recovered, diameter within ±50%
Median diameter error +2.2%
Breached craters are missed by design: they do not close
Mars Global Mosaic · Interim presentation
13

## Slide 14
CRATERS
Closed depressions ≥ 1 km across ±60°
465,354 closed depressions ≥ 1 km, from an 11-hour run
Against Robbins: 15.3% are catalogued craters at ≥ 1 km, 62.2% at ≥ 5 km, 83.1% at ≥ 20 km
Their density barely follows the catalogued craters (r −0.11); below ~5 km it follows the DEM's sharpness
Good for large craters and as prompts for review; for crater counts, Robbins is the reference
Mars Global Mosaic · Interim presentation
14

## Slide 15
CHANNELS
Channels across ±60°
969,822 routed channel segments; orders 3–5 drawn
60.5% of stream cells discarded as fill artefact (Ius alone: 56%)
89.8% lie on ground under 2°, so the plateau channels are DEM noise
No channel reference exists at ±60°, so the network is not scored
Mars Global Mosaic · Interim presentation
15

## Slide 16
TYPE AREAS
Ius Chasma: candidates to digitise
Fill raised the canyon floor 2,077 m; 56% of the first channel network was artefact
188 channel candidates are steep and rock-floored; the review starts with them
Only 11% of the 1,685 closed depressions ≥ 1 km match a Robbins crater, so they are prompts for review
Mars Global Mosaic · Interim presentation
16

## Slide 17
TYPE AREAS
Athabasca Valles: the second type area
Flood lava once mapped as a water channel; the USGS map calls it Late Amazonian volcanic (lAv)
Built the same way as Ius: 3,283 channel candidates, 409 of them rock-floored
Catalogued craters: 1,122 per million km² on lAv, against 1,760 and 2,183 on the older units
The diurnal-contrast index does not track calibrated TES inertia here (r ≈ 0); Viking albedo does (−0.55)
Mars Global Mosaic · Interim presentation
17

## Slide 18
CLASSIFICATION
Checking the first two classifications
The 29 Sep map follows its 4096-px processing tiles instead of the terrain
The 30 Sep map is mostly elevation: elevation alone reproduces 62% of it
Both problems led to the corrected stack, with no elevation band and slope in degrees
Mars Global Mosaic · Interim presentation
18

## Slide 19
CLASSIFICATION
Landforms at ±60°, scored on labels the model never saw
512 hand-drawn polygons in whole 15° blocks: 329 train the SVM, 183 are held out
Published map, 200 m, 11 × 11 majority (2.2 km): 73.8%, κ 0.58 held out; one class everywhere: 58.6%
Halving the cell bought no accuracy: 69.9% raw at 200 m, 70.5% at 400 m
Normal Ground and cratered terrain hold up; lava tube does not (2% user's accuracy)
Mars Global Mosaic · Interim presentation
19

## Slide 20
CLASSIFICATION
The landform classes against the USGS geologic map
Each cell: how much more often a class occurs in a unit group than across ±60° (×1 = no link)
"Lava tube" gathers on volcano flanks and aprons (×3.30, ×4.29), not on volcanic plains (×0.84)
76% of the volcanic plains come out Normal Ground
The classes follow terrain, so lava flows are taken from the geologic map
Mars Global Mosaic · Interim presentation
20

## Slide 21
CLASSIFICATION
Does thermal infrared improve the classification?
Slope and relief alone: 68.6%, κ 0.51 held out; all seven bands: 67.0%, κ 0.50
The thermal bands add +1.3 points (95% interval +0.6 to +2.2), small but clear of zero
Without terrain, visible and thermal score below one class everywhere (58.6%)
The labels are landforms, so terrain decides them; testing thermal IR properly needs material labels
Mars Global Mosaic · Interim presentation
21

## Slide 22
CLASSIFICATION
The thermal gain, confirmed with ArcGIS Pro's own SVM
Pro's SVM retrained over all of ±60° with the published settings, leaving out one band group at a time
Thermal adds +1.36 points at 200 m (+0.46 to +2.47) and +1.97 at 400 m (+1.08 to +3.35)
Thermal helps craters and hills and hurts lava tube; leaving out visible, or both groups, leaves the score tied
Terrain alone ties the overall score but gets only 34 of 124 crater polygons right
Mars Global Mosaic · Interim presentation
22

## Slide 23
DEEP LEARNING
Deep learning, 1: a detector that draws boxes
RetinaNet on the 7-band stack, trained on the training blocks only, scored on the 183 held-out polygons
Crater: 41.9% of polygons found, 87.6% of boxes right, against 71.1% for always naming Crater
Normal Ground: 22.7% found, 56.9% right; hills and lava tube never named
Retrained with the backbone unfrozen for 30 epochs, it names hills but finds only 4.5% of Normal Ground, so it is no better
Mars Global Mosaic · Interim presentation
23

## Slide 24
DEEP LEARNING
Deep learning, 2: a U-Net maps terrain provinces
A U-Net pixel classifier on the same stack and labels, over all of ±60°; a second pass, offset 128 px, removes its tile seams
Held out: 98.9%, κ 0.980, against the published SVM map's 73.8%, κ 0.583, under the same scorer
Lava tube becomes usable: 77.1% user's accuracy, against 2.4% for the SVM
It maps provinces rather than single landforms: its 'Crater' covers 82.6% of the ring around named craters. The SVM map stays the published one
Mars Global Mosaic · Interim presentation
24

## Slide 25
HYPOTHESES
Do the infrared mosaics show lava-flow edges Viking misses? (H1)
NOT SETTLED: THE MAP IS TOO COARSE
905 profiles across 10 of the geologic map's lava contacts at Athabasca: does each band tell the units apart?
Every band does only slightly better than chance (10%): Viking red 12.3%, day IR 21.0%
Day IR leans toward H1, but the intervals overlap (difference +8.7 points, −1.7 to +18.1)
Contacts on a 1:20 M map are kilometres wide; H1 is retested on margins digitised at 100 m
Mars Global Mosaic · Interim presentation
25

## Slide 26
HYPOTHESES
Do volcanic channels differ from fluvial ones? (H2)
NOT SUPPORTED AT STAGE 1
Channel candidates, Ius Chasma (fluvial) against Athabasca Valles (volcanic): 2,588 and 3,272
H2 expected the volcanic channels to be steeper; they are shallower (median 1.4 against 10.2 m per km)
Thermal response tells the two apart no better than chance (AUC 0.50)
Not supported at stage 1: the window sets the gradient, not the origin. Reviewed channels retest it
Mars Global Mosaic · Interim presentation
26

## Slide 27
HYPOTHESES
Is the composite more stable than a single band? (H3)
NOT SUPPORTED
Iso Cluster trained on the west and the east half of Ius, compared over the whole window
The composites are the least reproducible inputs: 0.40 and 0.38, against 0.61–0.89 for single bands
They give the smoothest maps, only just ahead of Viking (0.85 against 0.84)
H3 is not supported
Mars Global Mosaic · Interim presentation
27

## Slide 28
HYPOTHESES
How many tributary orders does 100 m resolve? (Q5)
THE DEM CANNOT ANSWER IT
Channel thresholds from 1 to 500 km² of catchment at Ius Chasma
The highest stream order follows the threshold: 5 at 1 km², 3 at 50 km², 2 at 500 km²
Only 30.8–36.7% of first-order streams lie on slopes ≥ 2°, at every threshold
The order count reflects the threshold chosen, so the DEM cannot answer Q5
Mars Global Mosaic · Interim presentation
28

## Slide 29
WHAT THE MEASUREMENTS LIMIT
Project Issues and Hurdles
The thermal signal is weak where it can be checked
The THEMIS mosaics follow calibrated TES thermal inertia only weakly inside 15° blocks (|r| ≈ 0.1) and not at all across the planet; Viking albedo follows it (r −0.31 to −0.36). In the classification the thermal bands add 1.3–2.0 points, with two classifiers.
The landform classes are terrain classes
Slope and relief alone score as well as all seven bands. On the geologic map the classes sit where terrain puts them, and "lava tube" lands on volcano flanks rather than lava plains.
Five "Crater" labels are volcanoes
Arsia Mons alone is 31% of the held-out Crater area; a seven-class scheme is proposed for the final.
Lava flows come from the geologic map
These bands cannot tell volcanic plains from other plains, and a fifth "volcanic" class scored below chance. Lava flows are taken from the USGS map's volcanic units.
Closed depressions are not a crater count
Of the candidates ≥ 1 km, 11–13% in the type areas and 15.3% across ±60° are catalogued craters; from 5 km up most are (62.2%). The Robbins catalogue (385,049 craters) is the crater reference.
Four hypotheses tested, none supported
No band separates the geologic map's lava contacts much better than chance, though the map is too coarse to settle H1; the volcanic channels are shallower, and thermal response separates nothing (H2, stage 1); the composite's classes are the least reproducible input (H3); no channel threshold keeps first-order streams on real slopes (Q5).
Mars Global Mosaic · Interim presentation
29

## Slide 30
WHAT SLOWS THE WORK
Project Issues and Hurdles
The review has not started
0 of 9,287 candidates are reviewed; H1 and H2 wait for digitised features.
428.7 GB on one USB drive
Reads cap near 112 MB/s, and the drive has dropped off mid-write, so big outputs are built on internal disk first.
Solved since September
Three coordinate frames, the z-factor defect, four failed global composites, the missing night mosaic, a defective DEM column at 180°.
Mars Global Mosaic · Interim presentation
30

## Slide 31
FOR THE FINAL
Next Steps
1
Review the 9,287 machine candidates at Ius Chasma and Athabasca Valles; draw breached craters and lava margins
2
Score the candidates against the reviewed features on the validation sheet; retest H1 on digitised margins and H2 on reviewed channels with their origin set
3
Move to seven classes: review the 1,086 proposed labels, rerun the SVM and U-Net, and score both maps on the same held-out polygons
4
Deep learning: set aside validation blocks before any further tuning, so the held-out blocks stay a clean test
8–26 Oct
Pyramids, ±60° crater and channel pass, 200 m map, T1 in Pro, the deep-learning detector and U-Net; seven classes proposed
26 Oct
Interim data cut; later results go to the final report
27 Oct – 22 Nov
Review and digitising; the seven-class labels and maps; H1 and H2 on digitised features; data freeze
10 Nov
Interim presentation
23 Nov – 4 Dec
Final report and presentation
8 Dec
Final due
Mars Global Mosaic · Interim presentation
31